## Slide 1: GPIO driver validation report
Baranidharan KARUPPUSAMY

## Slide 2: Driver development using BDD
GPIO driver + App code (Submodule to delivered)
Test code
(Main.c to validate the driver & App)
Inputs.txt (Data for IO in 10ms samples)
generate_inputs.py
Outputs.txt
parse_log.py
Plot (used for validation report)
Start here

## Slide 3
Sample input data
Data for IO in 10ms samples
1 for HIGH
0 for LOW
First data PB1
Second data PB2
Generated programmatically

## Slide 4
Parsing output data
Output data parse to extract input, output & timing information to dataframe
Dataframe plotted for inference

## Slide 5
Sample output data
Output by test code in 10 ms task
T -> time in milliseconds since program start
I -> GPIO input status
  _ indicates LOW and ^ indicates HIGH state
G & R are GPIO output status for GREEN and RED LESs
  O indicates ON and X indicates OFF state
Also shows code execution flow as nested log
50ms debounce, log entry is output after the actual process of inputs

## Slide 6: Actual driver code to be used in complex app

## Slide 7: Active high PB1
After valid debouce (50 ms) of pb1 callback toggles green LED
Input without valid debouce of pb1 ignored

## Slide 8: PB2
After first pb2 activation red LED toggles at 1000ms interval
Before pb2 activation red LED toggles at 500ms interval
After second pb2 activation red LED toggles at 2000ms interval
After third pb2 activation red LED toggles rollback at 500ms interval

## Slide 9: Active low PB1
After valid debouce of pb1 callback toggles green LED
Input without valid debouce of pb1 ignored

## Slide 10: Future improvements
Currently input are generated programmatically, this can be further enhanced using python behave that would make defining dynamic behaviour much easier
Output is validated by manual inspection with behave can be validated systematically and validate against system requirement.
Then this can be integrated to build process (CICD) validating against spec each time code being modified.
This approach will enhance software system functional reliability considerably, next time no need to debug entire system for a trivial software bug which can be easily capture in the CICD build process itself.